## Slide 1: Data representation
CAOS 2019

## Slide 2: Analog signal -> Digital signal

## Slide 3: Inputs/Outputs states
“0” – voltage < threshold_0 (~0.7 V)
“1” – voltage > threshold_1 (~2 V)
Undefined
High impedance

## Slide 4: PC organization

## Slide 5: Intel 8080

## Slide 6: Intel 8085

## Slide 7: System architecture
Von Neumann architecture – same address space for instructions and data (Almost every processor)
Harvard architecture – separate address space for instructions and data (microcontrollers)
Modified Harvard architecture – less separated memory, but still concurrent buses

## Slide 8: Data encoding
1 byte – minimal addressable memory unit
CPU can read 1 machine word per clock tick
Bit order depends on processor
Byte order (inside a word) also depends on processor

## Slide 9: BE vs LE
BigEndian – natural order of bytes: most significant bytes first. (Standard for networking)
LittleEndian – byte order in x86: less significant bytes first. Common for x86

## Slide 10: Structs alignment
Blocks that have lengths divisible to machine word length are more convenient for CPU
Fields in structs (and classes) aligned to borders

## Slide 11: Data representation
Unsigned integers
Signed integers – no standard in C, however most processor use two’s complement

## Slide 12
Unsigned | Binary | Direct encoding | Complement encoding
0 | 000 | 0 | 0
1 | 001 | 1 | 1
2 | 010 | 2 | 2
3 | 011 | 3 | 3
4 | 100 | -0 | -4
5 | 101 | -1 | -3
6 | 110 | -2 | -2
7 | 111 | -3 | -1

## Slide 13: Integer oveflow
X + Y – sum(X, Y) =: C > 0 -overflow
C = 0 iff sum(X, Y) > X && sum(X, Y) > Y
CPU can catch overflow (OF)
However C can’t check it explicitly

## Slide 14: String representation
ASCII – 7 bit for Latin
[128, 255] for national characters
Universal UTF8 encoding with variable code length
2 or 4 bytes per symbol

## Slide 15: man 7 utf8
0x00000000 - 0x0000007F: 0xxxxxxx
0x00000080 - 0x000007FF: 110xxxxx 10xxxxxx
0x00000800 - 0x0000FFFF: 1110xxxx 10xxxxxx 10xxxxxx
0x00010000 - 0x001FFFFF: 11110xxx 10xxxxxx 10xxxxxx 10xxxxxx
0x00200000 - 0x03FFFFFF: 111110xx 10xxxxxx 10xxxxxx 10xxxxxx 10xxxxxx
0x04000000 - 0x7FFFFFFF: 1111110x 10xxxxxx 10xxxxxx 10xxxxxx 10xxxxxx 10xxxxxx

## Slide 16: wchar_t
sizeof(wchar_t)==4 (Unix) or 2 (MSVC)
wchar_t usage guarantees correct [] indexing
Utf8 is good only for sequential processing

## Slide 17: Float representation (IEEE 754)